## Slide 1: So you want to Cad a part?

## Slide 2: Bringing geometry into your layout
Each major assy has “-000” Layout as the main file where you “do” the cad
To bring in reference geometry:
  Double click on layout file to enter in context
  Under Assemblies, open “Wave Geometry linker”
  Select the things you want, bodies, planes, sketches etc
  Objects show up in your assembly as “linked”
You can bring parts from all other layouts adjacent assemblies, not just the top one!

## Slide 3
So you cadded all the parts in the layout file as bodies, cool!
Make an empty part file Following “C-10X-00Y PART NAME”, where X matches the layout and Y is a new number.
Put empty part file in the layout using “add component
Using wave link, bring in just the body you want
Hide the datum coordinates, and add the body to the reference set
And that’s it!
Your layout at the end should contain all parts in the assembly AND any subassemblies
Making Your Part File

## Slide 4: Assemblies (-50X)
Assemblies live in parallel to the layout system
Assemblies NEVER use constraints
  They break all the time
  MOVE by constraint is what you want
Only add parts using absolute coordinates, and they’ll automatically be in the right place in space
Using assembly patterns is OK and highly recommended!
Adding cots parts is annoying, we’ll figure out what we want to do
  Maybe have a COTS KIT to contain the mess to one thing

## Slide 5: Nx can't find the part I want to load
A drawback of using github is it saves parts to the local path of the computer it was saved on, so you need to switch to using search folders
  Search “Assembly load options” in top bar
  Select from seach folders
  Select top level folder of the repo
This is annoying but It'll take 2 seconds every time you open NX
For this reason, we will be saving all PNs to one big folder, annoying but it means you only have to add 1 folder every time

## Slide 6: Saving and Pushing to github
This system lets us work on cad in parallel as long as we’re working in different layouts
If we save over each other, we will lose work!
What we can do to avoid this
  Push / Pull as often as you can, it takes 2 seconds!!!!!!!
  Message the team if you’re going to change the top level layout
  Stay vocal about what cad you’re working in
  Don’t save a layout if you think someone else is working on it
This wasn’t an issue previously bc we knew generally who was working on what, so I think we’ll be ok

## Slide 7: PN TREE / FLOW
C100-000
LAYOUT
C101-000
SUB LAYOUT
C102-000
SUB LAYOUT
C101-00X
PART X
C102-00X
PART X
C101-501
SUB ASSEMBLY
C100-501
TOP ASSEMBLY
C101-501
SUB ASSEMBLY